## Slide 1: An Introduction to CUDA/OpenCL and Graphics Processors
Bryan Catanzaro, NVIDIA Research

## Slide 2: Heterogeneous Parallel Computing
Throughput Optimized GPU
Scalable Parallel Processing
Latency Optimized CPU
Fast Serial Processing

## Slide 3: Latency vs. Throughput
Specifications | Ivy Bridge EX (Xeon E7-8890v2) | Kepler (Tesla K40)
Processing Elements | 15 cores, 2 issue, 8 way SIMD @2.8 GHz | 15 SMs, 6 issue, 32 way SIMD @745 MHz
Resident Strands/Threads (max) | 15 cores, 2 threads, 8 way SIMD: 240 strands | 15 SMs, 64 SIMD vectors, 32 way SIMD: 30720 threads
SP GFLOP/s | 672 | 4291
Memory Bandwidth | 85 GB/s | 288 GB/s
Register File | xx kB (?) | 3.75 MB
Local Store/L1 Cache | 960 kB | 960 kB
L2 Cache | 3.75 MB | 1.5 MB
L3 Cache | 37.5 MB | -
Ivy Bridge EX 22nm, 541 mm2
Kepler GK110

## Slide 4: Why Heterogeneity?
Different goals produce different designs
  Throughput cores: assume work load is highly parallel
  Latency cores: assume workload is mostly sequential
Latency goal: minimize latency experienced by 1 thread
  lots of big on-chip caches
  extremely sophisticated control
Throughput goal: maximize throughput of all threads
  lots of big ALUs
  multithreading can hide latency … so skip the big caches
  simpler control, cost amortized over ALUs via SIMD

## Slide 5: SIMD
a
Single Instruction Multiple Data architectures make use of data parallelism
We care about SIMD because of area and power efficiency concerns
  Amortize control overhead over SIMD width
Parallelism exposed to programmer & compiler
b
c
a2
a1
b2
b1
c2
c1
+
+
SISD
SIMD
width=2

## Slide 6: SIMD: Neglected Parallelism
OpenMP / Pthreads / MPI all neglect SIMD parallelism
Because it is difficult for a compiler to exploit SIMD
How do you deal with sparse data & branches?
  Many languages (like C) are difficult to vectorize
Most common solution:
  Either forget about SIMD
    Pray the autovectorizer likes you
  Or instantiate intrinsics (assembly language)
  Requires a new code version for every SIMD extension

## Slide 7: A Brief History of x86 SIMD Extensions
MMX
SSE
SSE2
SSE3
SSSE3
SSE4.1
SSE4.2
AVX
AVX+FMA
AVX2
8*8 bit Int
4*32 bit FP
2*64 bit FP
Horizontal ops
8*32 bit FP
3 operand
256 bit Int ops,
Gather
MIC
512 bit
3dNow!
SSE4.A
SSE5

## Slide 8: What to do with SIMD?
Neglecting SIMD is becoming more expensive
  AVX: 8 way SIMD, Xeon Phi: 16 way SIMD, Nvidia: 32 way SIMD, AMD: 64 way SIMD
This problem composes with thread level parallelism
We need a programming model which addresses both problems
4 way SIMD (SSE)
16 way SIMD (Phi)

## Slide 9: The CUDA Programming Model
CUDA is a programming model designed for:
  Heterogeneous architectures
  Wide SIMD parallelism
  Scalability
CUDA provides:
  A thread abstraction to deal with SIMD
  Synchronization & data sharing between small thread groups
CUDA programs are written in C++ with minimal extensions
OpenCL is inspired by CUDA, but HW & SW vendor neutral

## Slide 10: Hello World: Vector Addition
//Compute vector sum C=A+B
//Each thread performs one pairwise addition
__global__ void vecAdd(float* a, float* b, float* c) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
c[i] = a[i] + b[i];
}
int main() {
//Run N/256 blocks of 256 threads each
vecAdd<<<N/256, 256>>>(d_a, d_b, d_c);
}

## Slide 11: Hierarchy of Concurrent Threads
Parallel kernels composed of many threads
  all threads execute the same sequential program
Threads are grouped into thread blocks
  threads in the same block can cooperate
Threads/blocks have unique IDs
  Thread t
t0 t1 … tN
Block b

## Slide 12: What is a CUDA Thread?
Independent thread of execution
  has its own program counter, variables (registers), processor state, etc.
  no implication about how threads are scheduled
CUDA threads might be physical threads
  as mapped onto NVIDIA GPUs
CUDA threads might be virtual threads
  might pick 1 block = 1 physical thread on multicore CPU

## Slide 13: What is a CUDA Thread Block?
Thread block = a (data) parallel task
  all blocks in kernel have the same entry point
  but may execute any code they want
Thread blocks of kernel must be independent tasks
  program valid for any interleaving of block executions

## Slide 14: CUDA Supports:
Thread parallelism
  each thread is an independent thread of execution
Data parallelism
  across threads in a block
  across blocks in a kernel
Task parallelism
  different blocks are independent
  independent kernels executing in separate streams

## Slide 15: Synchronization
Threads within a block may synchronize with barriers
  … Step 1 … __syncthreads(); … Step 2 …
Blocks coordinate via atomic memory operations
  e.g., increment shared queue pointer with atomicInc()
Implicit barrier between dependent kernels
  vec_minus<<<nblocks, blksize>>>(a, b, c);
  vec_dot<<<nblocks, blksize>>>(c, c);

## Slide 16: Blocks must be independent
Any possible interleaving of blocks should be valid
  presumed to run to completion without pre-emption
  can run in any order
  can run concurrently OR sequentially
Blocks may coordinate but not synchronize
  shared queue pointer: OK
  shared lock: BAD … can easily deadlock
Independence requirement gives scalability

## Slide 17: Scalability
Manycore chips exist in a diverse set of configurations
Chart: 
| 8300GS | 9400M | 8800GTX | GTX285
Size | 1 | 2 | 16 | 30
Number of SMs
CUDA allows one binary to target all these chips
Thread blocks bring scalability!

## Slide 18: Memory model
Thread
Per-thread Local Memory
Block
Per-block Shared Memory

## Slide 19: Memory model
Kernel 0
Kernel 1
Sequential
Kernels
…
…
Per Device Global Memory

## Slide 20: Memory model
Host Memory
Device 0 Memory
Device 1 Memory
cudaMemcpy()

## Slide 21: Hello World: Vector Addition
//Compute vector sum C=A+B
//Each thread performs one pairwise addition
__global__ void vecAdd(float* a, float* b, float* c) {
int i = blockIdx.x * blockDim.x + threadIdx.x;
c[i] = a[i] + b[i];
}
int main() {
//Run N/256 blocks of 256 threads each
vecAdd<<<N/256, 256>>>(d_a, d_b, d_c);
}

## Slide 22: Hello World: Managing Data
int main() {
int N = 256 * 1024;
float* h_a = malloc(sizeof(float) * N);
//Similarly for h_b, h_c. Initialize h_a, h_b
float *d_a, *d_b, *d_c;
cudaMalloc(&d_a, sizeof(float) * N);
//Similarly for d_b, d_c
cudaMemcpy(d_a, h_a, sizeof(float) * N, cudaMemcpyHostToDevice);
//Similarly for d_b
//Run N/256 blocks of 256 threads each
vecAdd<<<N/256, 256>>>(d_a, d_b, d_c);
cudaMemcpy(h_c, d_c, sizeof(float) * N, cudaMemcpyDeviceToHost);
}

## Slide 23: CUDA: Minimal extensions to C/C++
Declaration specifiers to indicate where things live
__global__ void KernelFunc(...); // kernel callable from host
__device__ void DeviceFunc(...); // function callable on device
__device__ int GlobalVar; // variable in device memory
__shared__ int SharedVar; // in per-block shared memory
Extend function invocation syntax for parallel kernel launch
KernelFunc<<<500, 128>>>(...); // 500 blocks, 128 threads each
Special variables for thread identification in kernels
dim3 threadIdx; dim3 blockIdx; dim3 blockDim;
Intrinsics that expose specific operations in kernel code
  __syncthreads(); // barrier synchronization
Notes: Simple model, extending C only where necessary

## Slide 24: Using per-block shared memory
Variables shared across block
  __shared__ int *begin, *end;
Scratchpad memory
  __shared__ int scratch[BLOCKSIZE];
  scratch[threadIdx.x] = begin[threadIdx.x]; // … compute on scratch values … begin[threadIdx.x] = scratch[threadIdx.x];
Communicating values between threads
  scratch[threadIdx.x] = begin[threadIdx.x];
  __syncthreads(); int left = scratch[threadIdx.x - 1];
Per-block shared memory is faster than L1 cache, slower than register file
It is relatively small: register file is 2-4x larger
Block
Shared

## Slide 25: CUDA: Features available on GPU
Double and single precision (IEEE compliant)
Standard mathematical functions
  sinf, powf, atanf, ceil, min, sqrtf, etc.
Atomic memory operations
  atomicAdd, atomicMin, atomicAnd, atomicCAS, etc.
These work on both global and shared memory

## Slide 26: CUDA: Runtime support
Explicit memory allocation returns pointers to GPU memory
  cudaMalloc(), cudaFree()
Explicit memory copy for host ↔ device, device ↔ device
  cudaMemcpy(), cudaMemcpy2D(), ...
Texture management
  cudaBindTexture(), cudaBindTextureToArray(), ...
OpenGL & DirectX interoperability
  cudaGLMapBufferObject(), cudaD3D9MapVertexBuffer(), …

## Slide 27: OpenCL
OpenCL is supported by AMD {CPUs, GPUs} and Nvidia
  Intel, Imagination Technologies (purveyor of GPUs for iPhone/etc.) are also on board
OpenCL’s data parallel execution model mirrors CUDA, but with different terminology
OpenCL has rich task parallelism model
  Runtime walks a dependence DAG of kernels/memory transfers

## Slide 28: CUDA and OpenCL correspondence
Thread
Thread-block
Global memory
Constant memory
Shared memory
Local memory
__global__ function
__device__ function
__constant__ variable
__device__ variable
__shared__ variable
Work-item
Work-group
Global memory
Constant memory
Local memory
Private memory
__kernel function
no qualification needed
__constant variable
__global variable
__local variable

## Slide 29: OpenCL and SIMD
SIMD issues are handled separately by each runtime
AMD GPU Runtime
  Vectorizes over 64-way SIMD
    Prefers scalar code per work-item (on newer AMD GPUs)
AMD CPU Runtime
  No vectorization
    Use float4 vectors in your code (float8 when AVX appears?)
Intel CPU Runtime
  Vectorization optional, using float4/float8 vectors still good idea
Nvidia GPU Runtime
  Full vectorization, like CUDA
    Prefers scalar code per work-item

## Slide 30: Imperatives for Efficient CUDA Code
Expose abundant fine-grained parallelism
  need 1000’s of threads for full utilization
Maximize on-chip work
  on-chip memory orders of magnitude faster
Minimize execution divergence
  SIMT execution of threads in 32-thread warps
Minimize memory divergence
  warp loads and consumes complete 128-byte cache line

## Slide 31: Mapping CUDA to Nvidia GPUs
CUDA is designed to be functionally forgiving
  First priority: make things work. Second: get performance.
However, to get good performance, one must understand how CUDA is mapped to Nvidia GPUs
Threads: each thread is a SIMD vector lane
Warps: A SIMD instruction acts on a “warp”
  Warp width is 32 elements: LOGICAL SIMD width
Thread blocks: Each thread block is scheduled onto an SM
  Peak efficiency requires multiple thread blocks per SM

## Slide 32: Mapping CUDA to a GPU, continued
The GPU is very deeply pipelined to maximize throughput
This means that performance depends on the number of thread blocks which can be allocated on a processor
Therefore, resource usage costs performance:
  More registers => Fewer thread blocks
  More shared memory usage => Fewer thread blocks
It is often worth trying to reduce register count in order to get more thread blocks to fit on the chip
  For Kepler, target 32 registers or less per thread for full occupancy

## Slide 33: Occupancy (Constants for Kepler)
The Runtime tries to fit as many thread blocks simultaneously as possible on to an SM
  The number of simultaneous thread blocks (B) is ≤ 8
The number of warps per thread block (T) ≤ 32
Each SM has scheduler space for 64 warps (W)
  B * T ≤ W=64
The number of threads per warp (V) is 32
B * T * V * Registers per thread ≤ 65536
B * Shared memory (bytes) per block ≤ 49152/16384
  Depending on Shared memory/L1 cache configuration
Occupancy is reported as B * T / W

## Slide 34: Profiling
nvvp (nvidia visual profiler) useful for interactive profiling
export CUDA_PROFILE=1 in shell for simple profiler
  Then examine cuda_profile_*.log for kernel times & occupancies

## Slide 35: SIMD & Control Flow
Nvidia GPU hardware handles control flow divergence and reconvergence
  Write scalar SIMD code, the hardware schedules the SIMD execution
  One caveat: __syncthreads() can’t appear in a divergent path
    This may cause programs to hang
  Good performing code will try to keep the execution convergent within a warp
    Warp divergence only costs because of a finite instruction cache

## Slide 36: Memory, Memory, Memory
A many core processor ≡ A device for turning a compute bound problem into a memory bound problem Kathy Yelick, Berkeley
Lots of processors, only one socket
Memory concerns dominate performance tuning

## Slide 37: Memory is SIMD too
Virtually all processors have SIMD memory subsystems
0
1
2
3
4
5
6
7
cache line width
This has two effects:
  Sparse access wastes bandwidth
0
1
2
3
4
5
6
7
2 words used, 8 words loaded:
¼ effective bandwidth
  Unaligned access wastes bandwidth
0
1
2
3
4
5
6
7
4 words used, 8 words loaded:
½ effective bandwidth

## Slide 38: Coalescing
GPUs and CPUs both perform memory transactions at a larger granularity than the program requests (“cache line”)
GPUs have a “coalescer”, which examines memory requests dynamically from different SIMD lanes and coalesces them
To use bandwidth effectively, when threads load, they should:
  Present a set of unit strided loads (dense accesses)
  Keep sets of loads aligned to vector boundaries

## Slide 39: Data Structure Padding
Multidimensional arrays are usually stored as monolithic vectors in memory
Care should be taken to assure aligned memory accesses for the necessary access pattern
(row major)
L
J

## Slide 40: SoA, AoS
Different data access patterns may also require transposing data structures
Array of Structs
Structure of Arrays
T
The cost of a transpose on the data structure is often much less than the cost of uncoalesced memory accesses
Use shared memory to handle block transposes

## Slide 41: Efficiency vs Productivity
Productivity is often in tension with efficiency
  This is often called the “abstraction tax”
C
Low level
Fast
Efficiency Language
Less Productive
High level
Slow
Productivity Language
More Productive

## Slide 42: Efficiency and Productivity
Parallel programming also gives us a “concrete tax”
  How many of you have tried to write … which is faster than a vendor supplied library?
Divergent Parallel Architectures means performance portability is increasingly elusive
Low-level programming models tie you to a particular piece of hardware
And if you’re like me, often make your code slow
  My SGEMM isn’t as good as NVIDIA’s
FFT
SGEMM
Sort
Scan
Reduce

## Slide 43: The Concrete Tax: A Case Study
OpenCL experiment on CPU and GPU
Two optimized reductions, one for CPU, one for GPU
Running GPU code on CPU:
  40X performance loss compared to CPU optimized code
Running CPU on GPU:
  ~100X performance loss compared to GPU optimized code
Concrete code led to overspecialization
Wide Parallel Reduction (good for GPU)
Narrow Parallel
Reduction (good for CPU)

## Slide 44: Abstraction, cont.
Reduction is one of the simplest parallel computations
Performance differentials are even starker as complexity increases
There’s a need for abstractions at many levels
  Primitive computations (BLAS, Data-parallel primitives)
  Domain-specific languages
These abstractions make parallel programming more efficient and more productive
Use libraries whenever possible!
  CUBLAS, CUFFT, Thrust

## Slide 45
A C++ template library for CUDA
  Mimics the C++ STL
Containers
  On host and device
Algorithms
  Sorting, reduction, scan, etc.
Notes: C++ STL is a very well thought-out collection of generic algorithms
Interface is already familiar to programmers
Thrust uses nvcc to instantiate templated CUDA kernels from generic templated specifications

## Slide 46: Diving In
#include <thrust/host_vector.h>
#include <thrust/device_vector.h>
#include <thrust/sort.h>
#include <cstdlib>
int main(void)
{
// generate 32M random numbers on the host
thrust::host_vector<int> h_vec(32 << 20);
thrust::generate(h_vec.begin(), h_vec.end(), rand);
// transfer data to the device
thrust::device_vector<int> d_vec = h_vec;
// sort data on the device (846M keys per sec on GeForce GTX 480)
thrust::sort(d_vec.begin(), d_vec.end());
// transfer data back to host
thrust::copy(d_vec.begin(), d_vec.end(), h_vec.begin());
return 0;
}
Notes: this is a complete Thrust program
Thrust is a header library – all the functionality is accessed by #including the appropriate Thrust header file
This program is compiled with nvcc as per usual, no special tools are required

## Slide 47: Objectives
Programmer productivity
  Build complex applications quickly
Encourage generic programming
  Leverage parallel primitives
High performance
  Efficient mapping to hardware

## Slide 48: Containers
Concise and readable code
  Avoids common memory management errors
// allocate host vector with two elements
thrust::host_vector<int> h_vec(2);
// copy host vector to device
thrust::device_vector<int> d_vec = h_vec;
// write device values from the host
d_vec[0] = 13;
d_vec[1] = 27;
// read device values from the host
std::cout << "sum: " << d_vec[0] + d_vec[1] << std::endl;
Notes: Vectors automatically release memory when they go out of scope
Abstracts CUDA runtime API (cudaMalloc, cudaMemcpy)

## Slide 49: Iterators
Pair of iterators defines a range
// allocate device memory
device_vector<int> d_vec(10);
// declare iterator variables
device_vector<int>::iterator begin = d_vec.begin();
device_vector<int>::iterator end = d_vec.end();
device_vector<int>::iterator middle = begin + 5;
// sum first and second halves
int sum_half1 = reduce(begin, middle);
int sum_half2 = reduce(middle, end);
// empty range
int empty = reduce(begin, begin);

## Slide 50: Iterators
Iterators act like pointers
// declare iterator variables
device_vector<int>::iterator begin = d_vec.begin();
device_vector<int>::iterator end = d_vec.end();
// pointer arithmetic
begin++;
// dereference device iterators from the host
int a = *begin;
int b = begin[3];
// compute size of range [begin,end)
int size = end - begin;

## Slide 51: Iterators
Encode memory location
  Automatic algorithm selection
// initialize random values on host
host_vector<int> h_vec(100);
generate(h_vec.begin(), h_vec.end(), rand);
// copy values to device
device_vector<int> d_vec = h_vec;
// compute sum on host
int h_sum = reduce(h_vec.begin(), h_vec.end());
// compute sum on device
int d_sum = reduce(d_vec.begin(), d_vec.end());

## Slide 52: Algorithms
Elementwise operations
  for_each, transform, gather, scatter …
Reductions
  reduce, inner_product, reduce_by_key …
Prefix-Sums
  inclusive_scan, inclusive_scan_by_key …
Sorting
  sort, stable_sort, sort_by_key …

## Slide 53: Algorithms
Standard operators
// allocate memory
device_vector<int> A(10);
device_vector<int> B(10);
device_vector<int> C(10);
// transform A + B -> C
transform(A.begin(), A.end(), B.begin(), C.begin(), plus<int>());
// transform A - B -> C
transform(A.begin(), A.end(), B.begin(), C.begin(), minus<int>());
// multiply reduction
int product = reduce(A.begin(), A.end(), 1, multiplies<int>());

## Slide 54: Algorithms
Standard data types
// allocate device memory
device_vector<int> i_vec = ...
device_vector<float> f_vec = ...
// sum of integers
int i_sum = reduce(i_vec.begin(), i_vec.end());
// sum of floats
float f_sum = reduce(f_vec.begin(), f_vec.end());

## Slide 55: Custom Types & Operators
struct negate_float2
{
__host__ __device__
float2 operator()(float2 a)
{
return make_float2(-a.x, -a.y);
}
};
// declare storage
device_vector<float2> input = ...
device_vector<float2> output = ...
// create function object or ‘functor’
negate_float2 func;
// negate vectors
transform(input.begin(), input.end(), output.begin(), func);
Notes: We can implement “micro-kernels” as c++ functors

## Slide 56: Custom Types & Operators
// compare x component of two float2 structures
struct compare_float2
{
__host__ __device__
bool operator()(float2 a, float2 b)
{
return a.x < b.x;
}
};
// declare storage
device_vector<float2> vec = ...
// create comparison functor
compare_float2 comp;
// sort elements by x component
sort(vec.begin(), vec.end(), comp);
Notes: A predicate for sorting implemented as a functor

## Slide 57: Interoperability
Convert iterators to raw pointers
// allocate device vector
thrust::device_vector<int> d_vec(4);
// obtain raw pointer to device vector’s memory
int * ptr = thrust::raw_pointer_cast(&d_vec[0]);
// use ptr in a CUDA C kernel
my_kernel<<< N / 256, 256 >>>(N, ptr);
// Note: ptr cannot be dereferenced on the host!

## Slide 58: Recap
Containers manage memory
  Help avoid common errors
Iterators define ranges
  Know where data lives
Algorithms act on ranges
  Support general types and operators

## Slide 59: Explicit versus implicit parallelism
CUDA is explicit
  Programmer’s responsibility to schedule resources
  Decompose algorithm into kernels
  Decompose kernels into blocks
  Decompose blocks into threads
Kernel 1
…
Kernel 2
…
…

## Slide 60: Explicit versus implicit parallelism
SAXPY in CUDA
__global__
void SAXPY(int n, float a, float * x, float * y)
{
int i = blockDim.x * blockIdx.x + threadIdx.x;
if (i < n)
y[i] = a * x[i] + y[i];
}
SAXPY <<< n/256, 256 >>>(n, a, x, y);

## Slide 61: Explicit versus implicit parallelism
SAXPY in CUDA
__global__
void SAXPY(int n, float a, float * x, float * y)
{
int i = blockDim.x * blockIdx.x + threadIdx.x;
if (i < n)
y[i] = a * x[i] + y[i];
}
SAXPY <<< n/256, 256 >>>(n, a, x, y);
Decomposition

## Slide 62: Explicit versus implicit parallelism
SAXPY in Thrust
// C++ functor replaces __global__ function
struct saxpy {
float a;
saxpy(float _a) : a(_a) {}
__host__ __device__
float operator()(float x, float y) {
return a * x + y;
}
};
transform(x.begin(), x.end(), y.begin(), y.begin(), saxpy(a));

## Slide 63: Implicitly Parallel
Algorithms expose lots of fine-grained parallelism
  Generally expose O(N) independent threads of execution
  Minimal constraints on implementation details
Programmer identifies opportunities for parallelism
  Thrust determines explicit decomposition onto hardware
Finding parallelism in sequential code is hard
  Mapping parallel computations onto hardware is easier
Notes: General strategy
Programmer identifies and exposes lots of parallelism via API
E.g. semantics of thrust::reduce() lets us reorder the reduction however we see fit
Runtime automatically

## Slide 64: Productivity Implications
Consider a serial reduction
// sum reduction
int sum = 0;
for(i = 0; i < n; ++i)
sum += v[i];

## Slide 65: Productivity Implications
Consider a serial reduction
// product reduction
int product = 1;
for(i = 0; i < n; ++i)
product *= v[i];

## Slide 66: Productivity Implications
Consider a serial reduction
// max reduction
int max = 0;
for(i = 0; i < n; ++i)
max = std::max(max,v[i]);
Notes: This kind of code replication is a natural thing to do
C programmers probably wouldn’t even think of this operation as a reduction, just iteration

## Slide 67: Productivity Implications
Compare to low-level CUDA
int sum = 0;
for(i = 0; i < n; ++i)
sum += v[i];
__global__
void block_sum(const float *input,
float *per_block_results,
const size_t n)
{
extern __shared__ float sdata[];
unsigned int i = blockIdx.x * blockDim.x + threadIdx.x;
// load input into __shared__ memory
float x = 0;
if(i < n)
{
x = input[i];
...
Notes: Ad hoc replication isn’t scalable in parallel codes as it is in serial codes

## Slide 68: Leveraging Parallel Primitives
Use sort liberally
data type | std::sort | tbb::parallel_sort | thrust::sort
char | 25.1 | 68.3 | 3532.2
short | 15.1 | 46.8 | 1741.6
int | 10.6 | 35.1 | 804.8
long | 10.3 | 34.5 | 291.4
float | 8.7 | 28.4 | 819.8
double | 8.5 | 28.2 | 358.9
Intel Core i7 950
NVIDIA GeForce 480
Notes: Lession: use
Sorting 32M keys on each platform - performance measured in millions of keys per second
CPU – Intel Core i7 950 @ 3.07 GHz
GPU – NVIDIA GeForce GTX 480
Lesson – use sorting instead of ad hoc binning b/c thrust::sort() is highly optimized

## Slide 69: Input-Sensitive Optimizations
Notes: Sorting 32M unsigned integers (uniformly distributed) with different numbers of occupied key bits
For example, Key Bits = 20 means all keys are in the range [0, 2^20)

## Slide 70: Leveraging Parallel Primitives
Combine sort with reduce_by_key
  Keyed reduction
  Bring like items together, collapse
  Poor man’s MapReduce
Can often be faster than custom solutions
  I wrote an image histogram routine in CUDA
  Bit-level optimizations and shared memory atomics
  Was 2x slower than thrust::sort + thrust::reduce_by_key
Notes: In the previous example we saw how to combine several Thrust algorithms (sort, unique, lower_bound) to implement a complex operation
This is a strategy that can be applied in general – using high level primitives

## Slide 71: Thrust on github
Quick Start Guide
Examples
Documentation
Mailing list (thrust-users)

## Slide 72: Summary
Throughput optimized processors complement latency optimized processors
Programming models like CUDA and OpenCL enable heterogeneous parallel programming
They abstract SIMD, making it easy to use wide SIMD vectors
CUDA and OpenCL encourages SIMD friendly, highly scalable algorithm design and implementation
Thrust is a productive C++ library for CUDA development

## Slide 73: Questions?
Bryan Catanzaro
bcatanzaro@nvidia.com
http://research.nvidia.com