## Slide 1: Using non-volatile memory (NVDIMM-N) as byte-addressable storage in Windows Server 2016
Tobias Klima
Program Manager

## Slide 2: The Case for Byte-Addressability
Problem
Storage Class Memory (NVDIMM-N) performance is not optimal in block mode (software overhead)
Opportunity
Utilize NVDIMM-N in byte-addressable (DAX) mode to achieve full performance potential
Approach
Memory-Map files on DirectAccess (DAX) volumes
NVDIMM-N supported in WS 2016
Exposes Block Interface (like a Disk), as well as byte-addressability option (DAX Volume)
SCM
Traditional
Storage
PCIe
CPU
SATA
SAS
NVDIMM-N
NVMe
AHCI
HBA
Memory

## Slide 3: DirectAccess Architecture
Overview
App has direct access to SCM via existing memory-mapping semantics
Updates directly modify SCM, Storage Stack not involved
DAX volumes identified through new flag
Characteristics
True device performance (no software overhead)
Byte-Addressable
Filter Drivers relying on I/O may not work or attach – no I/O, new volume flag
AV Filters can still operate (Windows Defender already updated)
SCM Disk Driver
SCM Bus Driver
Block Mode Application
Standard File API
SCM
DirectAccess Application
Load/Store
Operations
SCM-Aware File System (NTFS - DAX)
Application requests memory-mapped file
Enumerates NVDIMM
User Mode
Kernel Mode
Memory Mapped Region
Memory Mapped Region
Load/Store
Operations
DirectAccess Data Path
DirectAccess Setup Path

## Slide 4: Using DAX in WS 2016
DAX Volume Creation
Format n: /dax /q
Format-Volume –DriveLetter n –IsDAX $true
DAX Volume Identification
Is it a DAX volume?
call GetVolumeInformation(“C:\”, ...)
check lpFileSystemFlags for FILE_DAX_VOLUME (0x20000000)
Is the file on a DAX volume?
call GetVolumeInformationByHandleW(hFile, ...)
check lpFileSystemFlags for FILE_DAX_VOLUME (0x20000000)

## Slide 5: Using DAX in WS 2016
Memory Mapping
HANDLE hMapping = CreateFileMapping(hFile, NULL, PAGE_READWRITE, 0, 0, NULL);
LPVOID baseAddress = MapViewOfFile(hMapping, FILE_MAP_WRITE, 0, 0, size);
memcpy(baseAddress + writeOffset, dataBuffer, ioSize);
FlushViewOfFile(baseAddress, 0);
OR … use non-temporal instructions for NVDIMM-N devices for better performance
HANDLE hMapping = CreateFileMapping(hFile, NULL, PAGE_READWRITE, 0, 0, NULL);
LPVOID baseAddress = MapViewOfFile(hMapping, FILE_MAP_WRITE, 0, 0, size);
RtlCopyMemoryNonTemporal(baseAddress + writeOffset, dataBuffer, ioSize );

## Slide 6: Efficiency Gains with DAX Volumes
Outdated Assumptions
  Storage is no longer “slow”
  Creating, Tracking, Queueing, Completing I/O costs CPU cycles (context switches)
  Past tricks to speed up storage (caching, async I/O, queues), now slow us down
Direct Access
  NTFS Volume Mode (Regular vs. DAX) decided at Format Time
  No I/O, no queueing, no async reads/writes – just load/stores
  Flush user data via existing memory mapping APIs (FlushViewOfFile)
  … Or – use non-temporal instructions on NVDIMM-N
  Efficiency from DAX
  Less context switches on highly contested data structures
  Additional CPU cycles for more useful work

## Slide 7: NVDIMM-N Block vs. DAX Performance
Tobias Klima
Hardware Provided By:

## Slide 9: Adapting Apps for DAX – NVML
Overview
  Helper Library making use of SCM easier
  Maintained on GitHub, http://pmem.io/
  Abstracts OS specific dependencies
  Provides: key/value stores, logs, flushing, persistent heap, …
Use Case
  Alternative to handling flushing or creating SCM-aware data structures yourself
NVML on Windows
Work underway to port NVML to Windows

## Slide 10: Call to Action
Consider memory-mapped I/O on NVDIMM-N
How would you change your app, if you could do fast, reliable, synchronous updates?
What data(structures) do your apps use frequently? Which need the lowest possible access latencies?
Technical Resources
Memory Mapping - https://msdn.microsoft.com/en-us/library/ms810613.aspx
GetVolumeInformation - https://msdn.microsoft.com/en-us/library/windows/desktop/aa364993(v=vs.85).aspx
GetVolumeInformationByHandleW - https://msdn.microsoft.com/en-us/library/windows/desktop/aa964920(v=vs.85).aspx
Re-visit Build on Channel 9.
Continue your education at Microsoft Virtual Academy online.